## Slide 1
Introduction
One of the biggest woes of highway drivers is the amount of tolls along the road that require each vehicle to not only slow down significantly, but also pay sometimes up to $7-8 to the State. This inconvenience is protested on various levels, but since it's clear that the government must institute some type of toll system, we have decided to find a model that will at least optimize the time for each driver while still saving the State as much money as possible. Our problem, therefore, was to come up with a model that determines the optimal number of toll booths to be built on a given number of highway lanes.
We specifically modeled the arrival rates of cars coming into tollbooth plazas, the amount of time customers have to wait in line for service, the service time, and the merging/departure time through various diagrams, highway data, and personal experiences. These combined sources have led us to assume that each driver will find the shortest line to optimize their own personal waiting time before going through the booth at a constant service time of about 30 seconds. Based on the data we’ve collected, we used the Poisson Random Process to model both the arrival rates and waiting times. Our answer to this original concern can therefore be applied to a wide range of highways and interstates, and in turn will decrease the amount of traffic congestion while creating a convenient and profitable tollbooth system.
Variables
Assumptions
We assumed the following things in order to make a more simplistic and clear model which could be applied to a larger number of systems:
Using the Garden State Parkway for data will still create a system applicable to other highways and parkways.
There are both cash tollbooths run by human workers and EZ pass lanes which are electronic
Each car has no problems with paying and does not linger at the booth for too long, so the service time remains constant.
The drivers are responsible, reasonable, and follow precautions as well as possible.
The drivers drive at the speed limit when they are entering and exiting the plaza.
There is one waiting line and cars choose the first tollbooth that becomes free
Arrival times follow the Poisson Process
Methods and Analysis
The first equation is used to determine the constant figure for the cost per tollbooth. The average salary for a tollbooth worker is about $50,000 annually1, and that is balanced out by the income each tollbooth will earn. Therefore, the simple profit equation is: c=(50000)b-m where b is a unit of one booth and m is the income of the booths per year. This equation is important because it serves as a reminder that optimizing the number of tollbooths is only beneficial when the number of booths does not exceed the income of the plaza.
The second equation is far more complex, as it deals with the variable of time. To create the model of time, we have broken the plaza into five sections. Figure A, shown below, illustrates the markings of these segments.
FIGURE A: A REALISTIC DEPICTION OF A TOLLBOOTH PLAZA
As shown by the diagram, Section 1 of the plaza is reserved for the entrance of vehicles into the toll plaza. These arrival times are based on the data collected. Approximately 4,000 cars are served during morning rush hour from 9am to 10am. Approximately 1,000 cars are served from 11pm to 12am. It is assumed that arrival rates are constant during these hour long periods.
Section 2 of the diagram represents waiting time. It is assumed that there is one waiting line and that drivers will move from the waiting line to the first available tollbooth. Section 3 represents the service time, which we assume to be constant at 15 seconds per driver.
Equations
Merging Time
Section 4 of the diagram represents merging time. If the total number of cars is less than or equal to the number of lanes then the merging time will be 0, as these cars will simply travel through the merging zone in the time it takes to drive the distance, without changing lanes. (It takes about 3 seconds to drive a distance of 100 ft. with a speed limit of 25 mph). If the number of cars is greater than the number of lanes then the merging time will increase exponentially as the number of cars increases.
This is modeled by:
M(t) = B if n ≤ L
B+ea(c-L) if n > L,
where B is the time (in seconds) it takes to drive through zone 4 without merging, a is the time in minutes it takes to drive through zone 4 (B/60), L is the number of lanes, n is the number of tollbooths and c is the number of cars entering zone 4 in a minute. According to our data, the number of lanes is usually 2 so that is what we will assume. c is dependent of the volume of cars arriving and the service time of these cars. When all of the tollbooths are being used continually (ie. there is a line on the arrival side) the rate of cars entering the merging zone will be: c=kn, where k is the rate at which cars can be served and n is the number of toll booths. So, kn cars/minute could enter the merging zone.
The Limiting Case
The limiting case describes the situation where there is exactly 1 tollbooth per incoming lane of traffic. Based on data collected from the Garden State Parkway, an average of 118,000 cars pass through toll areas in a day, going in both directions. This corresponds with approximately 2,500 cars in an hour heading one way through a toll plaza. The average number of lanes on this highway is 4 (2 in each direction). The limiting case would therefore involve 2 tollbooths for the 2 lanes heading in one direction.
Based on the assumption that a toll booth can serve 2 cars/minute, 2 toll booths would be able to serve 4 cars/minute (240 cars/hour). However, a far greater number (~2,500 cars) arrive in that period of time. In this case, cars will continue to build up and the queue will never be cleared. After the first hour, the line of waiting cars will contain about 2,225 cars, after the second hour, ~4,450 cars, and so on. Based on the large build-up that will occur, this number of toll booths will not be sufficient for this volume of traffic.
Generalizations
In reality, many tollbooths have varying service times dependent on the drivers, operators, and other factors. We have assumed a service time of 15 seconds for cash tolls and 5 seconds for EZ pass lanes based on personal experience, but in reality, service times usually vary from driver to driver and even between different people running the toll booths. Any changes in how service time was calculated would change the results. Similarly, we assumed arrival rates to be constant over an hour period. This is probably not true in reality and therefore our results might be slightly off.
Also, different highways will have different volumes of drivers using EZ pass compared to drivers using cash tollbooths. We have assumed 60% of drivers use EZ pass based on personal experience. However, this may be an underestimate. More and more drivers are using EZ pass everyday and therefore the 60% we assume will gradually increase over time.
Conclusion
During morning rush hour we believe that 3 cash tollbooths and 5 EZ pass lanes are optimal. With this amount of tollbooths the toll plaza could serve a total of 72 drivers per minute. This is calculated by: # cash tolls*(1 min/15 sec) + # EZ pass lanes*(1 min/5 sec). Waiting time for cash tollbooths is only about 2 minutes and 45 seconds whereas waiting time for EZ pass lanes is less than 1 second. Merging time would be calculated using c=72 in this case [(3*2)+(5*12)] and thus merging time would be equal to about 40 seconds in this case. Thus, for drivers using cash tollbooths, the total time spent in zones 2-4 is about 3 minutes and 25 seconds and for EZ pass drivers it’s only about 41 seconds. We believe that both of these total times are reasonable during rush hour. Adding another cash tollbooth would decrease the waiting time for those drivers but increase the merging time for all drivers. It would also require more money to construct and maintain another tollbooth. Thus, since we believe that about 3.5 minutes is a reasonable time to take traveling through the toll plaza we believe that only 3 cash tollbooths and 5 EZ pass lanes are optimal.
From 11pm to 12am traffic flow is much less and therefore we believe that only 2 cash tollbooths and 1 EZ pass lane are needed to decrease waiting time and merging time to a reasonable amount. In this case about 20 drivers can be served per minute. Waiting time is about 8 seconds for cash drivers and 23 seconds for EZ pass drivers. An additional cash or EZ pass tollbooth in this case would only decrease the waiting time per driver by a few additional seconds. When calculating merging time we assumed that tollbooths would always be full and thus cars arriving into the merging area would be constant. However, during this period of much less traffic, this is probably not the case and therefore merging time would be less than before. Since the merging times in these scenarios are very small anyways we will use the same model to approximate merging times and assume that during lessened traffic flow these merging times will be a few seconds faster. In the merging time calculation for this situation, c=20 and thus merging time equals about 6 seconds. Thus all drivers will pass through the toll plaza in under 30 seconds. This is the minimum amount of tollbooths need to serve the average amount of drivers arriving every minute and thus this is the optimal amount of tollbooths.
These conclusions apply to the Garden State Parkway for the data used. However, this model can be applied to other highways by adjusting the average traffic per hour based on the data from that area.
Strengths and Weaknesses
This model is strong in that it simplifies the tollbooth problem so that it can be applied to a wide range of systems, all of which will have various factors that are likely covered in the four-part equation for time and the two-part equation for profit. By breaking down each section of a toll plaza, the model is successful in examining all different areas of tollbooths instead of assuming that waiting time is the only variable of time for drivers.
One of the model’s biggest weaknesses is that it does not account for weather changes. Often, in bad weather, there will be more crashes and drivers will drive more slowly through the plazas, causing for more congestion and longer waiting and merging times.